## Slide 1
OILGUARD
Forecasting-Based Early Warning of Abnormal Events in Oil Wells
Time Series Analysis on 19 Real Offshore Well Events (Petrobras 3W)
Audited Final Results | Class 2: Spurious Closure of DHSV

## Slide 2
The Industrial Challenge: Spurious DHSV Closure
Subsea Safety Valve Criticality: Downhole Safety Valves (DHSV) protect offshore platforms against uncontrolled well blowouts.
The Failure Mode (Class 2): Spurious closure suddenly chokes high-rate production conduits, causing rapid shut-in dynamics.
Limitations of Threshold Alarms: Current alarms only trigger when pressure crosses fixed lower limits—after the shut-in transient has already peaked.
Research Question: Can statistical forecasting residuals (e_t = y_t - y_hat_t) provide reliable early warnings 5-10 minutes in advance?
Baseline Comparator: A persistent Naive baseline (y_hat_t = y_{t-1}) is benchmarked against ARIMA and SARIMAX.

## Slide 3
Dataset Auditing & Preprocessing Integrity
Benchmark Scope: 2,228 files (1.87 GB) across 8 fault classes from offshore Brazilian basins.
Strict Gold Cohort (N=19): Audited 22 real-well Class 2 candidates; 19 gold events accepted. Excluded 3 files (including 1 constant flatline sensor file).
Sensor Selection: Target: P-TPT (downhole pressure, MPa); Exogenous: T-TPT (downhole temperature, degC).
Resampling & Preprocessing: Uniform 10s resampling with forward-fill limit of 6 raw samples; audited for flatline and long-gap anomalies.
Strict Chronological Partitioning: 60% Training (model fitting) | 20% Calibration (threshold calibration) | 20% Holdout + Full Transient (evaluation).

## Slide 4
Forecasting Accuracy: ARIMA & SARIMAX vs. Naive Baseline
ARIMA Test MAE: 0.0163 MPa (vs. Naive 0.0307 MPa) -> 47.1% Lower Forecasting Error!
ARIMA Test RMSE: 0.0524 MPa (vs. Naive 0.0781 MPa) -> 32.9% Lower Root Mean Squared Error!
ARIMA Test MAPE: 8.69% (vs. Naive 18.22%) -> Over 52% reduction in relative percentage error!
Validation R2 Score: ARIMA: 0.9107 | SARIMAX: 0.9025 | Naive Baseline: 0.7887
Key Finding: Statistical TSA models capture autocorrelation and exogenous thermal dynamics, drastically outperforming naive extrapolation.

## Slide 5
Audit of Early-Warning Evaluation Rules
The Anomaly in Default Rules: Under unoptimized static settings (q=0.99, p=3), Naive reported 7/19 early detections vs. 5/19 for ARIMA.
Audited Window Policy: Early warnings must strictly occur inside the 10-minute pre-event window [t_transient - 10m, t_transient).
False Alarm Separation: Alarms occurring during ordinary normal operation (before the pre-event window) are counted strictly as false alarms.
Lead Time Integrity: Lead times are calculated strictly from the pre-event alarm, guaranteeing bounded lead times (0 <= lead <= 10 min).
Denominator Integrity: All metrics use exactly the 19 evaluated gold events as the denominator.

## Slide 6
Unbiased Generalization: Leave-One-Event-Out Cross-Validation
Preventing Data Leakage: Retrospective grid search on holdout sets causes leakage. To guarantee unbiased evaluation, LOEO-CV was executed.
ARIMA LOEO-CV Detection: ARIMA achieves 42.1% early detection (8/19 events) with 5.10 minutes advance lead time.
Naive Baseline LOEO-CV: Naive baseline achieves 36.8% early detection (7/19 events) with 1.69 minutes lead time.
The Lead Time Advantage: ARIMA delivers over 3x the advance warning lead time of the baseline (5.10 min vs. 1.69 min)!
Conclusion: In honest cross-validation, statistical TSA models outperform the baseline in both detection rate and reaction window.

## Slide 7
Sensitivity Analysis & EWMA Residual Filtering
Grid Sensitivity Ceiling (p=1, q=0.95): ARIMA achieves 63.2% early detection (12/19) with 5.35 min lead time (empirical upper bound under post-hoc selection).
EWMA Filtered Residuals (lambda=0.3, q=0.975): ARIMA achieves 57.9% early warning (11/19) with 3.53 min lead time at 1.72 FA/hr.
Naive Comparison under EWMA: Naive achieves 42.1% (8/19) -> ARIMA provides a +15.8% advantage at identical false alarm rate.
Noise Attenuation: EWMA integrates persistent incipient drift while attenuating high-frequency turbulent sensor noise.
Pareto Frontier Verification: Non-dominated Pareto points programmatically calculated and verified on the 19 gold events.

## Slide 8
Operational Value & Qualified Conclusions
Actionable Lead Time: 5 minutes of advance lead time provides platform operators a potential window for diagnostic assessment and manual choke throttling.
Qualified Engineering Scope: Whether early warnings can reliably prevent water-hammer shocks or valve damage remains an engineering hypothesis requiring multiphase dynamic simulation (OLGA).
Reproducible Architecture: End-to-end Python pipeline complete with 10 unit tests, parameter config, and Jupyter walkthrough.
Core Takeaway: Statistical time series analysis delivers 47% better forecasting and superior advance warning lead time over persistence baselines.